## Slide 1: Improving WUE and NUE Through Irrigation Scheduling
Chad Godsey
Colorado Ag Water Workshop
Burlington, CO
Dec. 12, 2018

## Slide 2: Background of Godsey Precision Ag-PCM
Formed in 2012 after spending 7 years in Research and Extension at OSU.
Watched the lack of research being utilized in the real-world and often precision ag tools were not used to their full capability.
Connecting Precision Ag with boots on the ground agronomy

## Slide 3: Goals of PCM
Quantify water savings and improvement in WUE from VRI.
Improve Water Use Efficiency and Nitrogen Use Efficiency
Provide practical tools for producers and consultants to use
  Scalable
  Cost effective
  Simple to use
    Some level of customization
  Incorporate into larger platform

## Slide 4: Background
Started VRI Research in 2014
  Reinke
  Trimble
Made the switch from moisture probes to ET in 2015
Chart: CO 7 Water Received vs Cumm. ET

## Slide 5: Silt Loam Soil - NE
Chart: Capacitance vs ET Soil Moisture %

## Slide 6: Drain Gauge

## Slide 7: Drainage Totals 2017 and 2018
Chart: Date

## Slide 8: Available Water 0-24”
Zone Delineation

## Slide 10: Hydraulic Conductivity

## Slide 11: VRI Prescription 7/12
0.6”
0.5”
0.5”
0.6”
Average App. Rate – 0.67 in vs 0.75 in flat rate
11% reduction with this pass

## Slide 12
Chart: Daily Water Use

## Slide 13
Chart: Field B - Water Received Versus Cumm. ET

## Slide 14
Chart: Field C - Water Received Versus Cumm. ET

## Slide 15
Chart: Water Use for Growing Season

## Slide 16: Field C – Water Use Efficiency
Zone | Acres | Relative Yield | Water Applied | Rainfall received | Total Water | Water Use Efficiency
 |  |  | - - - - - - - in - - - - - - - |  |  | - - bu/in - -
1 | 70.3 | 100% | 13.9 | 6.82 | 20.71 | 11.4
2 | 27.2 | 100% | 13.9 | 6.82 | 20.71 | 11.4
3 | 3 | 103% | 13.2 | 6.82 | 20.06 | 12.1
4 | 8 | 102% | 13.2 | 6.82 | 20.06 | 12.0
5 | 6.3 | 102% | 13.2 | 6.82 | 20.06 | 12.1
6 | 11.5 | 94% | 13.2 | 6.82 | 20.06 | 11.1
7 | 2.8 | 98% | 13.2 | 6.82 | 20.06 | 11.5
Field Avg. |  |  |  |  | 20.52 | 11.43

## Slide 17: What we have observed 2016-2018
Year | Acre feet | Ac | Inches per acre from Irr. | Growing Season Rainfall | Water Use Efficiency
 |  |  |  | - in - | - bu/in -
2013 | 271 | 115 | 28.3 | 8.5 | 6.0
2014 | 184 | 115 | 19.2 | 14.9 | 7.0
2015 | 185 | 140 | 15.9 | 8.8 | 11.3
2016 | 116 | 140 | 10.0 | 9.7 | 10.7
Increase of WUE of 25%
Decrease in Water Use by 20%
*Soybeans in 2017 and water usage not available yet for 2018

## Slide 18: 2017 Results – How did PCM Perform?
17,500 sand acres located around Eckley and North of Wray in 2017, mostly Haxtun and Valent Sand
Average Water Pumped 14.8 inches
Average rainfall was 11.33 inches
Average Yield was 231.8 bu
  Yield ranged from 191 bu/ac to 283 bu/ac
WUE was 9.0 bu/inch

## Slide 19: 2017 Results – How did PCM Perform?
3500 hard ground acres located around Yuma and South of Eckley and Wray in 2017
Average Water Pumped 14.6 inches
Average rainfall was 10.4 inches
Average Yield was 249.1 bu
  Yield ranged from 222 bu/ac to 285 bu/ac
WUE was 9.9 bu/inch

## Slide 20: Case Study Farm 1
Consists of >1000 acres
  750 acres Silt Loam soil with WHC of 3.5-4.5” in surface 2 ft of soil
  260 acres Sandy-Sandy Loam soil with WHC of 1.0-1.75” in surface 2 ft of soil
Chart: Year
| 2009 | 2010 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017 | Ave (2009-2016) | Ave (2017-2018)
PN | 15.76 | 18.945 | 22.7375 | 27.885 | 21.5425 | 19.2225 | 13.115 | 13.6475 | 20.2969 | 13.465
Reduced irrigation by an average of 6.8”/ac
Rainfall averages
  2009-2015 ave. of 13.2”
  2016-2017 ave. of 12.8”

## Slide 21: Case Study Farm 2
Consists of >4500 acres
  All acres Sandy-Sandy Loam soil with WHC of 1.0-1.75” in surface 2 ft of soil
Reduced irrigation by an average of 4.43”/ac
Rainfall averages
  2009-2016 ave. of 13.0”
  2016-2017 ave. of 13.9”
Chart: Year
| 2009 | 2010 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | Ave (2009-2016) | Ave (2017-2018)
PN | 21.6346 | 23.5608 | 22.5758 | 24.6633 | 20.6504 | 20.3771 | 19.5379 | 15.43 | 18.4675 | 21.8571 | 17.426

## Slide 22: Yield Trends
Chart: Year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 1.0822 | 0.87102 | 0.99217 | 1.0538 | 0.8893 | 1.0558 | 1.0558
Farm 1
Farm 2
Chart: Year
| 2009 | 2010 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 0.9955 | 0.94887 | 0.94425 | 1.0314 | 1.0577 | 1.0269 | 0.94245 | 1.0094 | 1.0435

## Slide 23: Improving irrigation scheduling
Local Weather Data
  ET based
Soil texture
  Water holding capacity
    Unique water holding calculation for each soil
    For example, WHC of a “silt loam”, can vary as much as 1.5”

## Slide 24: Unique Items to PCM
Customizable limits and irrigation efficiencies
  Change target levels depending on the part of the season
Easy to Understand and interpret
Crop specific
Model crop growth when possible

## Slide 25: Weather Network

## Slide 26: App and Cloud-based System

## Slide 27: 2019
Integration with third party for irrigation and N
VRI

## Slide 28: Thank You
Chad Godsey, PhD
Owner, Godsey Precision Ag
Phone: 970-630-7732
Email: chad.godsey@godseyag.com
Web: godseyag.com
Twitter: @godseyag