## Slide 1
The “Use it or Lose It” Perception What are the Issues?

## Slide 2: Today’s Discussion
      Colorado water law is complicated and easily misunderstood

## Slide 3: Today’s Discussion
      Essence of a water right is its application to a beneficial use without waste

## Slide 4: Today’s Discussion
      Misleading adage “Use It or Lose It.”
      Can lead to a practice of diverting as much as possible, whether it’s needed or not
      ???

## Slide 5: Today’s Discussion
      Need to balance two concepts: duty of water and no waste

## Slide 6: Today’s Discussion
      Special Report No. 25 clarifies how the use or nonuse of a water right affects its value
      This is valuable in administration efforts

## Slide 7: Today’s Discussion
      Colorado water law is complicated and easily misunderstood
      Essence of a water right is its application to a beneficial use without waste
      Misleading adage “Use It or Lose It.”
      Can lead to a practice of diverting as much as possible, whether it’s needed or not
      Need to balance two concepts: duty of water and no waste
      Special Report No. 25 clarifies how the use or nonuse of a water right affects its value
      This is valuable in administration efforts

## Slide 8: Five Areas of Concern
      Maintaining a Conditional Water Right (Water Court)
      Administering an Absolute Water Right (Division of Water Resources)
      Abandoning a Water Right (Division of Water Resources, Water Court)
      Changing the Use of a Water Right (Water Court)
      Applying Intentional Conservation to a Water Right or Applying Water to an Undecreed Use (Division of Water Resources, Water Court)

## Slide 9
What is the Potential to Lose
the Water Right?

## Slide 10: Areas of Concern
      Maintaining a Conditional Water Right (Water Court)
        Potential to “lose it”: no “reasonable diligence,” speculation, can and will questions

## Slide 11: Areas of Concern
      Administering an Absolute Water Right (Division of Water Resources)
        Potential to “lose it”: generally none (always exceptions)

## Slide 12: Areas of Concern
      Abandoning a Water Right (Division of Water Resources, Water Court)
        Potential to “lose it”: nonuse (partial or full), intent to abandon

## Slide 13: Areas of Concern
      Changing the Use of a Water Right (Water Court)
        Potential to “lose it”: “loss” due to quantification based on use during representative study period; nearly always less than what could have happened within the decree

## Slide 14: Areas of Concern
      Applying Intentional Conservation to a Water Right or Applying Water to an Undecreed Use (Division of Water Resources, Water Court)
        Potential to “lose it”: none, if done with validation of effort (time is still a factor)

## Slide 15: For example…

## Slide 16: Five Areas of Concern
      Maintaining a Conditional Water Right (Water Court)
      Administering an Absolute Water Right (Division of Water Resources)
      Abandoning a Water Right (Division of Water Resources, Water Court)
      Changing the Use of a Water Right (Water Court)
      Applying Intentional Conservation to a Water Right or Applying Water to an Undecreed Use (Division of Water Resources, Water Court)

## Slide 17
A water right can be transferred to another use
Requires a legal/engineering process: “Change of Water Right”
    Ensure no injury to other water rights,
    No expansion of use.
Change of Water Right

## Slide 18
Consider a decreed water right for an irrigation ditch
Decree allows a diversion of 15 cfs for defined land
Change of Water Right

## Slide 19
Change of Use Example A
(average historic practice before change)
River
Ditch
10 cfs applied to Field
10 cfs
20 cfs

## Slide 20
cfs
Breakdown
River Flow
20 cfs
River Flow
10 cfs
Divert
10 cfs

## Slide 21
We own the farm and would like to sell our water to someone for a new use.
We are going to “dry up” our land.
Change of Use Example A

## Slide 22
Change of Use Example A
What is the measure of our water right – what are we allowed to transfer?

## Slide 23
Change of Use Example A
(average historic practice before change)
River
Ditch
10 cfs (1,000 ac-ft) applied to field
6 cfs (600 ac-ft)
consumed by the crop
4 cfs (400 ac-ft) returns to the river by surface or ground water
14 cfs
20 cfs
10 cfs
15 cfs decreed?

## Slide 24
cfs
Breakdown
River Flow
10 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
4 cfs
(400 ac-ft)
River Flow
20 cfs
River Flow
10 cfs
Divert
10 cfs

## Slide 25
cfs
Breakdown
River Flow
10 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
4 cfs
(400 ac-ft)
River Flow
20 cfs
River Flow
10 cfs
Divert
10 cfs

## Slide 26
Consumptive Use Portion
Chart: 
| Crop ET (ac-ft)
 | 600

## Slide 27
Return Flow Portion
Chart: 
| Reasonable Percolation (ac-ft) | Reasonable Tailwater (Ditch) (ac-ft) | Reasonable Runoff from Field (ac-ft) | Reasonable Ponding (ac-ft) | EXCESSIVE PERCOLATION (AC-FT) | EXCESSIVE TAILWATER (AC-FT) | EXCESSIVE RUNOFF (AC-FT) | EXCESSIVE PONDING (AC-FT)
 | 260 | 20 | 85 | 35 | 0 | 0 | 0 | 0

## Slide 28
Return Flow Portion
This irrigator has taken steps to eliminate waste
No excessive
return flow
Chart: 
| Reasonable Return Flow | WASTE
 | 400 | 0

## Slide 29
Back to the Change of Use Example A
What is the measure of our water right – what are we allowed to transfer?

## Slide 30
cfs
Breakdown
River Flow
10 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
4 cfs
(400 ac-ft)
River Flow
20 cfs
River Flow
10 cfs
Divert
10 cfs
Cannot be transferred to a new use
Can be transferred to a new use

## Slide 31
Change of Use Example A After change
River
Ditch
6 cfs (600 ac-ft) goes
to another use
4 cfs (400 ac-ft) is
returned to the river
14 cfs
20 cfs
10 cfs

## Slide 32: For example… Let’s tweak the example Divert an additional amount to “protect” our full decreed water right
(We think we should USE IT
so we don’t LOSE IT)

## Slide 33
Change of Use Example B before change
River
Ditch
15 cfs
(1500 ac-ft) applied to Field
6 cfs (600 ac-ft)
consumed by the crop
9 cfs (900 ac-ft) returns to the river by surface or ground water
14 cfs
20 cfs
5 cfs

## Slide 34
cfs
Breakdown
River Flow
20 cfs
River Flow
5 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
9 cfs
(900 ac-ft)
River Flow
5 cfs
Divert
15 cfs

## Slide 35
Breakdown
cfs
River Flow
5 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
9 cfs
(900 ac-ft)
River Flow
20 cfs
River Flow
5 cfs
Divert
15 cfs

## Slide 36
Consumptive Use Portion
Chart: 
| Crop ET (ac-ft)
 | 600

## Slide 37
Return Flow Portion
Chart: 
| Reasonable Percolation (ac-ft) | Reasonable Tailwater (Ditch) (ac-ft) | Reasonable Runoff from Field (ac-ft) | Reasonable Ponding (ac-ft) | EXCESSIVE PERCOLATION (AC-FT) | EXCESSIVE TAILWATER (AC-FT) | EXCESSIVE RUNOFF (AC-FT) | EXCESSIVE PONDING (AC-FT)
 | 80 | 20 | 250 | 35 | 40 | 100 | 250 | 125
Waste

## Slide 38
Return Flow Portion
Chart: 
| Reasonable Return Flow | WASTE
 | 385 | 515
Excessive Waste,
This practice has unnecessarily taken water from the river.
Deprives other water rights
Impacts the river

## Slide 39
Cannot be transferred to a new use; and we have a greater obligation
cfs
Breakdown
River Flow
5 cfs
Cons.Use
6 cfs
(600 ac-ft)
Ret. Flow
9 cfs
(900 ac-ft)
River Flow
20 cfs
River Flow
5 cfs
Divert
15 cfs
Cannot be transferred to a new use
Can be transferred to a new use

## Slide 40
River
Ditch
6 cfs goes to the
new use
9 cfs returns to the river
14 cfs
20 cfs
5 cfs
Change of Use Example B After change

## Slide 41
Change of Use Example B
The measure of a water right is still its historical consumptive use. That is limited by what the crop can consume.
We can transfer only the same 6 cfs (600 ac-ft/yr)
But now we need to leave behind the 9 cfs (900 ac-ft/yr) that was always diverted and has always returned
Waste
In addition, we have diverted water unnecessarily from the river. Statutory conflict and impacts to the river.
to the river.

## Slide 42: Synopsis from the Regulatory Perspective Historical Consumptive Use
      Colorado water law is complicated and easily misunderstood
      Essence of a water right is its application to a beneficial use without waste
      Misleading adage “Use It or Lose It.”
      Can lead to a practice of diverting as much as possible, whether it’s needed or not
      Need to balance two concepts: duty of water and no waste
      Special Report No. 25 clarifies how the use or nonuse of a water right affects its value
      This is valuable in administration efforts